## Slide 1: BRK-100 Operator Training
Assembly tools and how to use them - Cell 3

## Slide 2: FX-201 Locating Fixture
Holds bracket BRK-100 on two D8 dowel pins
Check the pins every shift - a bent pin gives a crooked bushing
Use the finger slots to lift the part out, never a screwdriver
Notes: Show the operator where the spare dowel pins are kept.

## Slide 3: PT-301 Bushing Press Punch
Pilot D10.02 guides bushing BU-12 straight into the bore
Press with AP-501 until the shoulder seats - do not exceed 4 kN
Worn pilot = loose bushings (NCR-0042). Pilot is checked weekly

## Slide 4: GA-401 Go/No-Go Pin Gauge
GO end D10.00 must enter the bore freely
NO-GO end D10.05 (groove on handle) must NOT enter
Record every check in the inspection log

## Slide 5: TW-101 Torque Wrench
Set to 9.5 Nm for the M6 screws SC-616
Tighten in a cross pattern, stop at the first click
Return the setting to 2 Nm after the shift to protect the spring

## Slide 6: Common mistakes
Pressing the bushing without the part seated on both dowel pins
Using the NO-GO end first and forcing it into the bore
Torque wrench TW-101 left at a high setting overnight